## Slide 1: Nav 3,3i & EOL OS
Stryker Apps & Risk calculation

## Slide 2: End-of-Life: Background & Details
As we all know Nav3 , Nav3i runs on Windows 8.1
Windows 8.1 reached the end of Mainstream support on January 9 , 2018
and will reach end of Extended support on January 10, 2023.
Businesses that continue to use outdated software risk exposure to security vulnerabilities.
Data breaches are one risk, as a hacker could take advantage of known vulnerabilities that are no longer being patched by the manufacturer to access sensitive information
The point is, you can’t count on any OEM(Microsoft) support once product reaches EOL. You’re on your own at that point for repairs, replacements, and/or upgrades.

## Slide 3: Cart Vuln(s) & Remed(s)
Red – Vulnerability ; Green – Remediation
V1. Apps from different sources (Stryker & 3rd party) can be installed & executed on Nav3i
R1. Using Application whitelisting, Ensure only authorized applications can be installed & Runs on Nav3i. Recommendation : Microsoft AppLocker3
V2. Unused/Unnecessary Services (or) daemons existing in Nav3i system
R2. The Nav3i OS Current configuration deactivate only couple of services (Browser & Distributed Link Tracking Client ) for the platform to be installed. Using Policy Settings (GPO (or)LPO) block more services
V3. Enabling of Remote Desktop support for Remote Service from Stryker
R3. Local Support instead of Remote Desktop Service.

## Slide 4: Cart Vuln(s) & Remed(s)
V4. Unauthorized Removable Device & Unrestricted access
R4. Virus scan ‘On Access’ shall be enabled for all drives including the DVD drive. Currently, it is not enabled for DVD Drive
V5. Unauthorized BIOS changes
R5. The BIOS setting already protected by password in current design
V6. Open Access to all the OS System Settings (Control Panel, Registry, command line & Others) with out restriction
R6. Admin access restriction to perform any system settings operation other than the HDO Operations (Even for Staff)
V7. Open/Unrestricted Access to perform any operation other than the Nav3i Operations (Even for Hospital Staff)
R7. Admin access restriction to perform any operation other than the HDO Operations (Even for Staff)

## Slide 5: Application Running on Nav3i & Risk calculation
Attack Vector (Threat) | Effect on Application with End-of-Life OS | Remarks
1. Internet Connectivity | Avoid Internet Connectivity to Nav3i | 
2. OS Updates | No Effect on Appl. functionality as Updates already blocked | 
3. Unauthorized USB/DVD Plugin | Microsoft Defender provides the scanning for connected devices | 
4. Outdated/Unsupported 3rd party Components in OS | OS team needs a plan to identify and not use them (or) implement alternatives | 
5. Remote Access | Remove the Remote Desktop support and provide local support | 

## Slide 6
Attack Vector (Threat) | Effect on Application with End-of-Life OS | Remarks
6. Recovery feature with system restore points | Application has no dependency to create restore points | 
7. Firewall & Virus Scanner | No Effect on Application | 
8. Active & UnUsed Services/Drivers | OS team needs a plan to identify and remove them (or) implement alternatives | 
9. Outdated Crypto algorithms | Outdated & Weak Algorithms need to be identified and removed from OS | 
10. Plain Sensitive data | sensitive data(Crypto & PHI) existing in the cart needs to be encrypted (Info Leakage) | 
11. Backup/Restore system configuration and data | Appl. Can be restored with this process. | 
12. Unnoticed malware | Regular scanning needs to be scheduled | 
13. Virus scanner Rules Update | Regular update needed through local support | 
14. Virus scanner Schedule | Regular scheduling required | 

## Slide 7: Current Nav3i scripts
defenderupdate.bat: updates virus scanner on login
disable_auto_signin.bat: disables auto-login on system shutdown for next system start
rc_dis.bat / rc_ena.bat: disables or enables remote keyboard and mouse on login / logout
wifi_on.bat / wifi_off.bat: enables / disables WLAN service from Application Manager

## Slide 8
END